## Slide 1: Course Teachers: Md. Rezaur Raihan Assistant Professor, Dept. of EEE & Md Arafat Hossain Assistant Professor, Dept. of EEE
Course No. : EEE 1108
Course Title : Basic Electrical Engineering Sessional
Credits: 1.5
Department of Electrical and Electronic Engineering
Khulna University of Engineering & Technology

## Slide 2
Syllabus:
Laboratory Works: Experiments based on Basic Electrical Engineering
Direct Current: Voltage and current, resistance and power, Laws of electrical circuits and methods of network analysis, Principles of dc measuring apparatus.
Alternating Current: Instantaneous and r.m.s. current, voltage and power, Average power for various combinations of R, L, and C circuits, Phasor representation of sinusoidal quantities, Introduction to three phase circuits.
Magnetism: Laws of magnetic fields and methods of solving simple magnetic circuits.
Electrical Machines: DC generators and alternators; Introduction to transformer and its operating principles; Operating principles of DC and stepper motors.

## Slide 3: List of Experiments:
No. | Name of the Experiments
01 | Familiarization with electrical elements and measuring instruments
02 | Study and verification of ohm’s law
03 | Study and verification of KVL and KCL
04 | Verification of superposition theorem
05 | Measurement of power in series and parallel circuit
06 | Determination of circuit parameters of an R-L series circuit

## Slide 4: List of Experiments :(contd.)
No. | Name of the Experiments
07 | Measurement of line voltage and phase voltage of a 3-φ system
08 | Determination of open circuit characteristics curve of a dc generator
09 | Speed control of a dc shunt motor by varying armature voltage keeping the field current constant (armature control method)
10 | Open circuit test and short circuit test of a 1-φ transformer
Notes: a branch of "Artificial Intelligence".

## Slide 5: Assessment criteria:
Attendance/Class Participation 10%
Lab Reports and Class Performance (Includes Lab Test, Lab viva) 50%
Quizzes/Viva Voce 20%
Central Viva 20%
Total 100%

## Slide 6
Exp. No. : 01
Name of the Experiment: Familiarization with electric meters and verification of ohm’s law

## Slide 7: Electric Meters:
Ammeter
Voltmeter
AVO meter, Commercially called Multimeter
Wattmeter

## Slide 8: Ammeter
Measures the amount of current flow through the branch of a circuit.
Types:
1. DC Ammeter
2. AC Ammeter
Circuit symbols

## Slide 9: Typical connection of Ammeter:
Ammeter Should always be connected in Series with Load

## Slide 10: Connection Diagram of Ammeter:

## Slide 11: Pictorial View of DC & AC Ammeter
DC Ammeter
AC Ammeter

## Slide 12: Voltmeter
Used to measure Electrical potential difference between two points in an electric circuit
Types:
1. DC Voltmeter
2. AC Voltmeter

## Slide 13: Connection Diagram of Voltmeter:
Voltmeter must be connected in Parallel with Load !!
Voltmeter
Load
Battery

## Slide 14: Connection Diagram of Voltmeter:

## Slide 15: Pictorial View of DC & AC Voltmeter
DC Voltmeter
AC Voltmeter

## Slide 16
Summary:
Connection of ammeter and Voltmeter in a circuit

## Slide 17
Question?
What happens when the ammeter is connected in parallel and voltmeter connected in series
V

## Slide 19: Multimeter/AVO meter:

## Slide 20: Wattmeter
Measures the Electric power (active/real power) in watts
Types:
1. Analog Wattmeter
2. Digital Wattmeter

## Slide 21: Schematic Diagram of Wattmeter:
Current coil (cc)
Measured Power, P=VI
Pressure coil (pc)
Current
Supply

## Slide 22: Connection Diagram of Wattmeter:

## Slide 23: Pictorial View of Wattmeter:

## Slide 24: Report Writing:
Objectives
Introduction
Apparatus Required
Experimental Setup or Circuit Diagram
Experimental Data
Calculation
Graphs /Vector Diagrams (if any)
Results and Discussion
Conclusion
Question & Answer
References

## Slide 25: Objectives:
Purpose of Experiment e.g.To be familiar with the working principle of various electric meters.
Should be mentioned in points

## Slide 26: Introduction:
Introductory Description. e.g. Why and where ammeter, voltmeter & wattmeter are used.
Written in one Para

## Slide 27: Description of the work:
Working principle and additional figures
Theoretical Background of the experiment

## Slide 28: Apparatus Required:
Should be mentioned in numbers
Name of Equipments with rating
Quantity

## Slide 29: Experimental Setup:
The diagram of the work
Specify the Equipments
Direction of current flow
Polarity (if any)

## Slide 30: Experimental Data:
Should be written in table
Draw Table using Pencil & Ruler.

## Slide 31: Calculation:
Elaborate Calculation of the whole work
Mark the outcomes of the calculation with square box which will be discussed in the discussion and conclusion.

## Slide 32: Graph/Vector Diagram:
Proper Scaling of axis
Encircle the plotted data points
Labeling [Units should be included]
Figure No. along with figure name should be mentioned

## Slide 33: Result & Discussion:
Discuss your results
Comparison between measured and ideal value.
Is there any deviation in your result from ideal value & why?
Mention numerical values of different quantities(if any).
Discuss your graphs along with the possible deviation in it (if any)
Use proper scaling for current and voltage in the vector diagram.

## Slide 34: Conclusion:
What have you learnt from this experiment?
What is the necessity of this experiment?
What is the way to abase the error [if any]

## Slide 35: Question and Answer:
Questions must be written in your report.
Relevant answer should be written.

## Slide 36: Reference:
Sources- you have used to write the report
For more references – write in numbers
e.g. [1] writer name, “source name”.
[2]……………..

## Slide 37: References of Today’s Experiment:
[1] B.L. Theraja, “A Textbook of Electrical Technology, Volume I”.
[2] Robert L. Boylestad, “Introductory Circuit Analysis”.

## Slide 38: Top page of Sessional Report: