## Slide 1: Number Systems and Arithmetic

## Slide 2: Introduction
In this lesson, we will study basic arithmetic operations in various number systems with a particular stress on the binary system.
we understand how to convert between binary and decimal numbers.
we are going to learn how to perform addition, subtraction, multiplication, and division with binary numbers.
So let’s ready for that

## Slide 3: Binary Numbers
It needs to represent only two states,On and Off.
A transistor circuit that is either on or off has two possible signal values and can be constructed to be extremely reliable.
A decimal number (5740.750)10 can be represented as follows
5*103 +7*102 +4*101+0*100+7*10-1+5*10-2
In general a number with decimal point is represented by a series of coefficients as follows:
a3a2a1a0 .a-1a-2a-3
Hence the actual number can be written as
103*a3 +102*a2+101*a1+100*a0+10-1*a-1+10-2*a-2+10-3*a-3

## Slide 4: Binary Numbers
The coefficient of binary system has two possible values 0 and 1.
Each coefficient ak is multiplied by 2k . So (11101.11)2 can be represented as
1*24+1*23+1*22+0*21+1*20+1*2-1+1*2‑2 = (29.75)10
In general a number expressed in base-r system has coefficients multiplied by power of r
an*rn+ an-1*rn-1+an-2*rn-2+an-3*rn-3+……….++a1*r1+a0+a-1*r-1++a-2*r-2+….+ a-m*r-m
Convert (403.5)5 to decimal
  4*52+0*51+3*50+5*5-1= (104)10
## Work for (4021.2)5=(511.4)10

## Slide 5: HexaDecimal Numbers
For Hexa decimal system (base 16), first ten digits are borrowed from decimal system.
and letters A, B, C,D,E and F are used for digits 10,11,12,13,14 and 15 respectively.
An example of hexadecimal system is
(C5F2.E1)16=12*163+5*162+15*161+2*160+14*16-1+1*16-2=(50674.9375)10
## work for (B65F)16=(46687)10

## Slide 6: Octal and Hexadecimal Numbers
Since 23 =8 and 24=16, each octal digits corresponds to three binary digits and each hexadecimal digit corresponds to four binary digits.
Conversion from Binary to Octal
Conversion from Binary to Hexadecimal

## Slide 7: Binary Addition
We need to learn four basic rules in order to perform binary addition.
These rules are listed in the table below.

## Slide 8: Binary Addition
Another tricks.

## Slide 9: Binary Addition
Example

## Slide 10: Binary Addition
Example

## Slide 11: Binary Subtraction
We need to learn four basic rules in order to perform binary subtraction.
These rules are listed in the table below.

## Slide 12: Binary Subtraction
Example

## Slide 13: Binary Multiplication
Binary multiplication is similar to decimal multiplication. It is simpler than decimal multiplication because only 0s and 1s are involved.
There are four rules of the binary multiplication.

## Slide 14: Binary Multiplication

## Slide 15: Binary Multiplication

## Slide 16: Binary Division
Binary division is similar to decimal division.
It is called as the long division procedure.

## Slide 17: Binary Division

## Slide 18: Binary Division

## Slide 19: Octal Addition
Following octal addition table will help you greatly to handle Octal addition.

## Slide 20: Octal Addition
Example

## Slide 21: Octal Subtraction
The subtraction of octal numbers follows the same rules as the subtraction of numbers in any other number system.
The only variation is in borrowed number.
In the decimal system, you borrow a group of 1010.
In the binary system, you borrow a group of 210.
In the octal system you borrow a group of 810.

## Slide 22: Octal Subtraction
Example

## Slide 23: Octal Multiplication and Division
Similar to binary multiplication and division.
Self study

## Slide 24: Hexadecimal Addition
Following hexadecimal addition table will help you greatly to handle Hexadecimal addition.

## Slide 25: Hexadecimal Addition
Example

## Slide 26: Hexadecimal Subtraction
The subtraction of hexadecimal numbers follows the same rules as the subtraction of numbers in any other number system.
The only variation is in borrowed number.
In the decimal system, you borrow a group of 1010.
In the binary system, you borrow a group of 210.
In the hexadecimal system you borrow a group of 1610.

## Slide 27: Hexadecimal Subtraction
Example

## Slide 28: Hexadecimal Multiplication and Division
Similar to binary multiplication and division.
Self study

## Slide 29
Any question?

## Slide 30
Complete Number System Arithmetic