## Slide 1: Complements

## Slide 2: Complements
Complements are used in digital computer for
  Simplifying the subtraction operations.
  Logical manipulations.
Two types of complements
  r’s complement
  (r-1)’s complement
Here r denotes the base for a number system (e.g. binary, octal).
When the value of r is substituted by 2, the two types receive the names 2’s and 1’s complement for binary numbers.

## Slide 3: r’s Complement(base 10)
Given a positive number N in base r with an integer part of n digits.
r’s complement of N is defined as rn – N for N ≠ 0.
example  10’s complement of (52520)10 ?
here n = 5, N = 52520
So the complement (52520)10  rn – N = 105 – 52520 = 47480
Very easy to calculate 

## Slide 4: r’s Complement(base 10)
Calculate 10’s complement of the number (0.3267)10.
There is no integer part. So how you will calculate?
But very easy to calculate, just think a little bit.

## Slide 5: r’s Complement(base 10)
Here n = 0.
So (0.3267)10  rn – N = 100 – 0.3267 = 0.6733.
Nice work done. 
Try it yourself
  (16273)10  ?
  (25.639)10  ?

## Slide 6: r’s Complement(base 2)
2’s complement of (101100)2 ?
Here n = 6.
So (101100)2  rn – N = (26)10 – (101100)2 = (1000000 - 101100)2 = 10100.
2’s complement of (0.0110)2 ?
Same as previously you have computed.
Try it yourself.

## Slide 7: r’s Complement(base 2)
2’s complement of (0.0110)2 ?
Here n = 0.
So (0.0110)2  rn – N = (20)10 – (0.0110)2 = (1 - 0.0110)2 = 0.1010.
Nice work done. 
Try it yourself
  (11011101)2  ?
  (11101.01101)10  ?

## Slide 8: r’s Complement
A simple trick to compute r’s complement within a short time.
How ?
The 10’s complement of a decimal number can be formed by leaving all least significant zeros unchanged, subtracting the first nonzero least significant digit from 10, and then subtracting all other higher significant digits from 9.
The 2’s complement can be formed by leaving all least significant zeros and the first nonzero digit unchanged, and then replacing 1’s by 0’s and 0’s by 1’s in all other higher significant digits.
Nice trick. isn't it??????????

## Slide 9: (r-1)’s Complement(base 10)
Given a positive number N in base r with an integer part of n digits and a fraction part of m digits.
(r-1)’s complement of N is defined as rn – r –m – N.
example  9’s complement of (25.639)10 ?
here n = 2, m = 3 and N = 25.639
So the complement (25.639)10  rn – r –m – N = 102 – 10 –3 – 25.639 = 74.360
Very easy to calculate 

## Slide 10: (r-1)’s Complement(base 10)
Find 9’s complement of (52520)10 ?
Find 9’s complement of (0.3267)10 ?

## Slide 11: (r-1)’s Complement(base 10)
(52520)10  105 – 10 –0 – 52520 = 99999 – 52520 = 47479.
(0.3267)10  100 – 10 –4 – 0.3267 = 0.9999 – 0.3267 = 0.6732.

## Slide 12: (r-1)’s Complement(base 2)
1’s complement of (101100)2 ?
Here n = 6, m = 0.
(101100)2  (26 – 2 –0)10 – (101100)2 = (111111 - 101100)2 = 010011.
1’s complement of (0.0110)2 ?
Here n = 0, m = 4.
(0.0110)2  (20 – 2 –4)10 – (0.0110)2 = (1 – 2 –4)10 – (0.0110)2 = 0.1001

## Slide 13: (r-1)’s Complement
A simple trick to compute r’s complement within a short time.
How ?
The 9’s complement of a decimal number can be formed by subtracting every digit from 9.
The 1’s complement can be formed by replacing 1’s by 0’s and 0’s by 1’s.
Nice trick. isn't it??????????

## Slide 14: r’s Complement(base 2) using (r-1)’s complement
Find 1’s complement of the number.
Add 1 to the Least Significant Bit (LSB) of the number.
2's complement = 1's complement + 1.

## Slide 15: r’s Complement(base 10) using (r-1)’s complement
Find 1’s complement of the number.
Add 1 to the Least Significant Bit (LSB) of the number.
10's complement = 9's complement + 1.
Let us take a decimal number 456, 9’s complement of this number will be

## Slide 16: Binary Subtraction
We will add two binary number. But the result is equivalence to the result if we subtract the two number.
Is it possible?

## Slide 17: Binary Subtraction
Yes we can do it.
But how??????

## Slide 18: Subtraction with r’s complement
 | 72532 | Minuend | M
─ | 03250 | Subtrahend | N

## Slide 19: Subtraction with r’s complement
Add the minuend M to the r’s complement of the subtrahend N.
Inspect the result obtained in step 1 for an end carry:
  If an end carry occurs, discard it.
  If an end carry does not occur, take the r’s complement of the number obtained in step 1 and place a negative sign in front.

## Slide 20: Subtraction with r’s complement
Using 10’s complement, subtract 72532 – 3250.
M | 72532 | 72532 | 69282
N | 03250 | 96750 | 
10’s complement | 96750 | 169282 | 
End Carry

## Slide 21: Subtraction with r’s complement
Using 10’s complement, subtract 3250 – 72532.
M | 03250 | 03250
N | 72532 | 27468
10’s complement | 27468 | 30718
10’s complement 30718 |  | ─69282
No End Carry

## Slide 22: Subtraction with r’s complement
Using 2’s complement, subtract 1010100 – 1000100.
M | 1010100 | 1010100
N | 1000100 | 0111100
2’s complement | 0111100 | 10010000
Answer |  | 0010000 10000
End Carry

## Slide 23: Subtraction with r’s complement
Using 2’s complement, subtract 1000100 – 1010100
M | 1000100 | 1000100
N | 1010100 | 0101100
2’s complement | 0101100 | 1110000
2’s complement 1110000 |  | 0010000 ─10000
No End Carry

## Slide 24: Subtraction with (r–1)’s complement
Add the minuend M to the (r–1)’s complement of the subtrahend N.
Inspect the result obtained in step 1 for an end carry.
  If an end carry occurs, add 1 to the least significant digit(end-around carry).
  If an end carry does not occur, take the (r–1)’s complement of the number obtained in step 1 and place a negative sign in front.

## Slide 25: Subtraction with (r–1)’s complement
Using 9’s complement, subtract 72532 – 3250.
M | 72532 | 72532 | 69282
N | 03250 | 96749 | 
9’s complement | 96749 | 169281 | 
 |  | + 1 | 
End Carry

## Slide 26: Subtraction with (r–1)’s complement
Using 9’s complement, subtract 3250 – 72532.
M | 03250 | 03250
N | 72532 | 27467
9’s complement | 27467 | 30717
9’s complement 30717 |  | ─69282
No End Carry

## Slide 27: Subtraction with (r–1)’s complement
Using 1’s complement, subtract 1010100 – 1000100.
M | 1010100 | 1010100 | 0010000
N | 1000100 | 0111011 | 
1’s complement | 0111011 | 10001111 | 
 |  | + 1 | 
End Carry

## Slide 28: Subtraction with (r–1)’s complement
Using 1’s complement, subtract 1000100 – 1010100
M | 1000100 | 1000100
N | 1010100 | 0101011
1’s complement | 0101011 | 1101111
1’s complement 1101111 |  | 0010000 ─1000
No End Carry

## Slide 29
Any question?

## Slide 30
Complete Number System